topology = routerless;

use_space_while_stall = 1;

router = rlBeta;
extension_buffers = 2;

routing_function = min;
network_file = rlConfig4.txt;
traffic = uniform;

sample_period = 100000;
injection_rate = 0.24;

ejectors = 2;
buffer_policy = private;
routing_delay = 0;

packet_size = 5;
wait_for_tail_credit = 0; //must be set to false
num_vcs = 1;
vc_buf_size = 5;
small_buf_size = 1;
big_buf_size = 5; //big must equal to vc_buf_size
output_to_file = 1;
output_file_name = runs/rlBetaUniformOutput;

END Configuration File: examples/rl-tradeoffs/rlBetaUniform-runs/only-packet-size/rlConfig4/packet5-4
The number of channels = 80
==========================================================
==========================================================
============ {---- Ring Configuration ----} ============
==========================================================
==========================================================

------------------ [ Router-to-Node ] -------------------
 --- 0 has BufState size = 2147483647
0 -to- 0
 --- 1 has BufState size = 2147483647
1 -to- 1
 --- 2 has BufState size = 2147483647
2 -to- 2
 --- 3 has BufState size = 2147483647
3 -to- 3
 --- 4 has BufState size = 2147483647
4 -to- 4
 --- 5 has BufState size = 2147483647
5 -to- 5
 --- 6 has BufState size = 2147483647
6 -to- 6
 --- 7 has BufState size = 2147483647
7 -to- 7
 --- 8 has BufState size = 2147483647
8 -to- 8
 --- 9 has BufState size = 2147483647
9 -to- 9
 --- 10 has BufState size = 2147483647
10 -to- 10
 --- 11 has BufState size = 2147483647
11 -to- 11
 --- 12 has BufState size = 2147483647
12 -to- 12
 --- 13 has BufState size = 2147483647
13 -to- 13
 --- 14 has BufState size = 2147483647
14 -to- 14
 --- 15 has BufState size = 2147483647
15 -to- 15

------------------- [ Rings List ] --------------------

Ring ID = 1
Ring List = [0, 1, 5, 9, 13, 12, 8, 4 ]
Ring ID = 2
Ring List = [3, 7, 11, 15, 14, 10, 6, 2 ]
Ring ID = 3
Ring List = [0, 1, 2, 6, 10, 14, 13, 12, 8, 4 ]
Ring ID = 4
Ring List = [3, 7, 11, 15, 14, 13, 9, 5, 1, 2 ]
Ring ID = 5
Ring List = [0, 4, 8, 12, 13, 14, 15, 11, 7, 3, 2, 1 ]
Ring ID = 6
Ring List = [0, 1, 2, 3, 7, 6, 5, 4 ]
Ring ID = 7
Ring List = [4, 5, 6, 7, 11, 10, 9, 8 ]
Ring ID = 8
Ring List = [8, 9, 10, 11, 15, 14, 13, 12 ]
Ring ID = 9
Ring List = [5, 6, 10, 9 ]
Ring ID = 10
Ring List = [5, 9, 10, 6 ]
At router 0 = 0
input 1 is a channel to 0 to 4 (Ring 1)
input 2 is a channel to 0 to 4 (Ring 3)
input 3 is a channel to 0 to 1 (Ring 5)
input 4 is a channel to 0 to 4 (Ring 6)
Output 1 is a channel from 0 to 1 (Ring 1)
Output 2 is a channel from 0 to 1 (Ring 3)
Output 3 is a channel from 0 to 4 (Ring 5)
Output 4 is a channel from 0 to 1 (Ring 6)
At router 1 = 1
input 1 is a channel to 1 to 0 (Ring 1)
input 2 is a channel to 1 to 0 (Ring 3)
input 3 is a channel to 1 to 5 (Ring 4)
input 4 is a channel to 1 to 2 (Ring 5)
input 5 is a channel to 1 to 0 (Ring 6)
Output 1 is a channel from 1 to 5 (Ring 1)
Output 2 is a channel from 1 to 2 (Ring 3)
Output 3 is a channel from 1 to 2 (Ring 4)
Output 4 is a channel from 1 to 0 (Ring 5)
Output 5 is a channel from 1 to 2 (Ring 6)
At router 2 = 2
input 1 is a channel to 2 to 6 (Ring 2)
input 2 is a channel to 2 to 1 (Ring 3)
input 3 is a channel to 2 to 1 (Ring 4)
input 4 is a channel to 2 to 3 (Ring 5)
input 5 is a channel to 2 to 1 (Ring 6)
Output 1 is a channel from 2 to 3 (Ring 2)
Output 2 is a channel from 2 to 6 (Ring 3)
Output 3 is a channel from 2 to 3 (Ring 4)
Output 4 is a channel from 2 to 1 (Ring 5)
Output 5 is a channel from 2 to 3 (Ring 6)
At router 3 = 3
input 1 is a channel to 3 to 2 (Ring 2)
input 2 is a channel to 3 to 2 (Ring 4)
input 3 is a channel to 3 to 7 (Ring 5)
input 4 is a channel to 3 to 2 (Ring 6)
Output 1 is a channel from 3 to 7 (Ring 2)
Output 2 is a channel from 3 to 7 (Ring 4)
Output 3 is a channel from 3 to 2 (Ring 5)
Output 4 is a channel from 3 to 7 (Ring 6)
At router 4 = 4
input 1 is a channel to 4 to 8 (Ring 1)
input 2 is a channel to 4 to 8 (Ring 3)
input 3 is a channel to 4 to 0 (Ring 5)
input 4 is a channel to 4 to 5 (Ring 6)
input 5 is a channel to 4 to 8 (Ring 7)
Output 1 is a channel from 4 to 0 (Ring 1)
Output 2 is a channel from 4 to 0 (Ring 3)
Output 3 is a channel from 4 to 8 (Ring 5)
Output 4 is a channel from 4 to 0 (Ring 6)
Output 5 is a channel from 4 to 5 (Ring 7)
At router 5 = 5
input 1 is a channel to 5 to 1 (Ring 1)
input 2 is a channel to 5 to 9 (Ring 4)
input 3 is a channel to 5 to 6 (Ring 6)
input 4 is a channel to 5 to 4 (Ring 7)
input 5 is a channel to 5 to 9 (Ring 9)
input 6 is a channel to 5 to 6 (Ring 10)
Output 1 is a channel from 5 to 9 (Ring 1)
Output 2 is a channel from 5 to 1 (Ring 4)
Output 3 is a channel from 5 to 4 (Ring 6)
Output 4 is a channel from 5 to 6 (Ring 7)
Output 5 is a channel from 5 to 6 (Ring 9)
Output 6 is a channel from 5 to 9 (Ring 10)
At router 6 = 6
input 1 is a channel to 6 to 10 (Ring 2)
input 2 is a channel to 6 to 2 (Ring 3)
input 3 is a channel to 6 to 7 (Ring 6)
input 4 is a channel to 6 to 5 (Ring 7)
input 5 is a channel to 6 to 5 (Ring 9)
input 6 is a channel to 6 to 10 (Ring 10)
Output 1 is a channel from 6 to 2 (Ring 2)
Output 2 is a channel from 6 to 10 (Ring 3)
Output 3 is a channel from 6 to 5 (Ring 6)
Output 4 is a channel from 6 to 7 (Ring 7)
Output 5 is a channel from 6 to 10 (Ring 9)
Output 6 is a channel from 6 to 5 (Ring 10)
At router 7 = 7
input 1 is a channel to 7 to 3 (Ring 2)
input 2 is a channel to 7 to 3 (Ring 4)
input 3 is a channel to 7 to 11 (Ring 5)
input 4 is a channel to 7 to 3 (Ring 6)
input 5 is a channel to 7 to 6 (Ring 7)
Output 1 is a channel from 7 to 11 (Ring 2)
Output 2 is a channel from 7 to 11 (Ring 4)
Output 3 is a channel from 7 to 3 (Ring 5)
Output 4 is a channel from 7 to 6 (Ring 6)
Output 5 is a channel from 7 to 11 (Ring 7)
At router 8 = 8
input 1 is a channel to 8 to 12 (Ring 1)
input 2 is a channel to 8 to 12 (Ring 3)
input 3 is a channel to 8 to 4 (Ring 5)
input 4 is a channel to 8 to 9 (Ring 7)
input 5 is a channel to 8 to 12 (Ring 8)
Output 1 is a channel from 8 to 4 (Ring 1)
Output 2 is a channel from 8 to 4 (Ring 3)
Output 3 is a channel from 8 to 12 (Ring 5)
Output 4 is a channel from 8 to 4 (Ring 7)
Output 5 is a channel from 8 to 9 (Ring 8)
At router 9 = 9
input 1 is a channel to 9 to 5 (Ring 1)
input 2 is a channel to 9 to 13 (Ring 4)
input 3 is a channel to 9 to 10 (Ring 7)
input 4 is a channel to 9 to 8 (Ring 8)
input 5 is a channel to 9 to 10 (Ring 9)
input 6 is a channel to 9 to 5 (Ring 10)
Output 1 is a channel from 9 to 13 (Ring 1)
Output 2 is a channel from 9 to 5 (Ring 4)
Output 3 is a channel from 9 to 8 (Ring 7)
Output 4 is a channel from 9 to 10 (Ring 8)
Output 5 is a channel from 9 to 5 (Ring 9)
Output 6 is a channel from 9 to 10 (Ring 10)
At router 10 = 10
input 1 is a channel to 10 to 14 (Ring 2)
input 2 is a channel to 10 to 6 (Ring 3)
input 3 is a channel to 10 to 11 (Ring 7)
input 4 is a channel to 10 to 9 (Ring 8)
input 5 is a channel to 10 to 6 (Ring 9)
input 6 is a channel to 10 to 9 (Ring 10)
Output 1 is a channel from 10 to 6 (Ring 2)
Output 2 is a channel from 10 to 14 (Ring 3)
Output 3 is a channel from 10 to 9 (Ring 7)
Output 4 is a channel from 10 to 11 (Ring 8)
Output 5 is a channel from 10 to 9 (Ring 9)
Output 6 is a channel from 10 to 6 (Ring 10)
At router 11 = 11
input 1 is a channel to 11 to 7 (Ring 2)
input 2 is a channel to 11 to 7 (Ring 4)
input 3 is a channel to 11 to 15 (Ring 5)
input 4 is a channel to 11 to 7 (Ring 7)
input 5 is a channel to 11 to 10 (Ring 8)
Output 1 is a channel from 11 to 15 (Ring 2)
Output 2 is a channel from 11 to 15 (Ring 4)
Output 3 is a channel from 11 to 7 (Ring 5)
Output 4 is a channel from 11 to 10 (Ring 7)
Output 5 is a channel from 11 to 15 (Ring 8)
At router 12 = 12
input 1 is a channel to 12 to 13 (Ring 1)
input 2 is a channel to 12 to 13 (Ring 3)
input 3 is a channel to 12 to 8 (Ring 5)
input 4 is a channel to 12 to 13 (Ring 8)
Output 1 is a channel from 12 to 8 (Ring 1)
Output 2 is a channel from 12 to 8 (Ring 3)
Output 3 is a channel from 12 to 13 (Ring 5)
Output 4 is a channel from 12 to 8 (Ring 8)
At router 13 = 13
input 1 is a channel to 13 to 9 (Ring 1)
input 2 is a channel to 13 to 14 (Ring 3)
input 3 is a channel to 13 to 14 (Ring 4)
input 4 is a channel to 13 to 12 (Ring 5)
input 5 is a channel to 13 to 14 (Ring 8)
Output 1 is a channel from 13 to 12 (Ring 1)
Output 2 is a channel from 13 to 12 (Ring 3)
Output 3 is a channel from 13 to 9 (Ring 4)
Output 4 is a channel from 13 to 14 (Ring 5)
Output 5 is a channel from 13 to 12 (Ring 8)
At router 14 = 14
input 1 is a channel to 14 to 15 (Ring 2)
input 2 is a channel to 14 to 10 (Ring 3)
input 3 is a channel to 14 to 15 (Ring 4)
input 4 is a channel to 14 to 13 (Ring 5)
input 5 is a channel to 14 to 15 (Ring 8)
Output 1 is a channel from 14 to 10 (Ring 2)
Output 2 is a channel from 14 to 13 (Ring 3)
Output 3 is a channel from 14 to 13 (Ring 4)
Output 4 is a channel from 14 to 15 (Ring 5)
Output 5 is a channel from 14 to 13 (Ring 8)
At router 15 = 15
input 1 is a channel to 15 to 11 (Ring 2)
input 2 is a channel to 15 to 11 (Ring 4)
input 3 is a channel to 15 to 14 (Ring 5)
input 4 is a channel to 15 to 11 (Ring 8)
Output 1 is a channel from 15 to 14 (Ring 2)
Output 2 is a channel from 15 to 14 (Ring 4)
Output 3 is a channel from 15 to 11 (Ring 5)
Output 4 is a channel from 15 to 14 (Ring 8)

==================== {---- END ----} ====================

==========================================================
==========================================================
============ {---- Starting Simulation ----} ============
==========================================================
==========================================================

Class 0:
Packet latency average = 7.4613
minimum = 1
maximum = 116
Network latency average = 5.69956
minimum = 1
maximum = 48
Slowest packet = 106
Flit latency average = 4.91099
minimum = 1
maximum = 48
Slowest flit = 151213
Fragmentation average = 0
minimum = 0
maximum = 0
Injected packet rate average = 0.239811
minimum = 0.23723 (at node 6)
maximum = 0.24131 (at node 10)
Accepted packet rate average = 0.239793
minimum = 0.23802 (at node 1)
maximum = 0.2417 (at node 11)
Injected flit rate average = 0.431436
minimum = 0.42516 (at node 5)
maximum = 0.43517 (at node 14)
Accepted flit rate average= 0.431409
minimum = 0.42502 (at node 1)
maximum = 0.43815 (at node 13)
Injected packet length average = 1.79906
Accepted packet length average = 1.79909
Total in-flight flits = 60 (0 measured)
latency change = 1
throughput change = 1
Class 0:
Packet latency average = 7.45064
minimum = 1
maximum = 116
Network latency average = 5.70364
minimum = 1
maximum = 48
Slowest packet = 106
Flit latency average = 4.91954
minimum = 1
maximum = 48
Slowest flit = 151213
Fragmentation average = 0
minimum = 0
maximum = 0
Injected packet rate average = 0.239663
minimum = 0.23806 (at node 1)
maximum = 0.24102 (at node 2)
Accepted packet rate average = 0.239654
minimum = 0.238245 (at node 6)
maximum = 0.24172 (at node 7)
Injected flit rate average = 0.430954
minimum = 0.42596 (at node 5)
maximum = 0.43559 (at node 8)
Accepted flit rate average= 0.430939
minimum = 0.427105 (at node 4)
maximum = 0.43602 (at node 7)
Injected packet length average = 1.79816
Accepted packet length average = 1.79817
Total in-flight flits = 49 (0 measured)
latency change = 0.00142991
throughput change = 0.00108919
Class 0:
Packet latency average = 7.47172
minimum = 1
maximum = 74
Network latency average = 5.69974
minimum = 1
maximum = 41
Slowest packet = 767300
Flit latency average = 4.91095
minimum = 1
maximum = 40
Slowest flit = 2002582
Fragmentation average = 0
minimum = 0
maximum = 0
Injected packet rate average = 0.240344
minimum = 0.23876 (at node 14)
maximum = 0.24375 (at node 6)
Accepted packet rate average = 0.240344
minimum = 0.23699 (at node 2)
maximum = 0.24538 (at node 15)
Injected flit rate average = 0.432884
minimum = 0.42588 (at node 14)
maximum = 0.44223 (at node 6)
Accepted flit rate average= 0.43288
minimum = 0.42745 (at node 13)
maximum = 0.44638 (at node 15)
Injected packet length average = 1.8011
Accepted packet length average = 1.80108
Total in-flight flits = 56 (0 measured)
latency change = 0.00282051
throughput change = 0.00448306
Warmed up ...Time used is 300000 cycles
Class 0:
Packet latency average = 7.45918
minimum = 1
maximum = 84
Network latency average = 5.71041
minimum = 1
maximum = 43
Slowest packet = 1151754
Flit latency average = 4.92865
minimum = 1
maximum = 43
Slowest flit = 2748938
Fragmentation average = 0
minimum = 0
maximum = 0
Injected packet rate average = 0.239686
minimum = 0.23671 (at node 15)
maximum = 0.24175 (at node 8)
Accepted packet rate average = 0.239677
minimum = 0.2369 (at node 12)
maximum = 0.24299 (at node 13)
Injected flit rate average = 0.431334
minimum = 0.42388 (at node 2)
maximum = 0.43647 (at node 8)
Accepted flit rate average= 0.431308
minimum = 0.42422 (at node 12)
maximum = 0.43695 (at node 13)
Injected packet length average = 1.79958
Accepted packet length average = 1.79954
Total in-flight flits = 101 (101 measured)
latency change = 0.00168064
throughput change = 0.00364444
Class 0:
Packet latency average = 7.47637
minimum = 1
maximum = 84
Network latency average = 5.70892
minimum = 1
maximum = 43
Slowest packet = 1151754
Flit latency average = 4.92744
minimum = 1
maximum = 43
Slowest flit = 2748938
Fragmentation average = 0
minimum = 0
maximum = 0
Injected packet rate average = 0.240179
minimum = 0.239015 (at node 2)
maximum = 0.241915 (at node 13)
Accepted packet rate average = 0.240179
minimum = 0.237715 (at node 0)
maximum = 0.242395 (at node 5)
Injected flit rate average = 0.432116
minimum = 0.427895 (at node 4)
maximum = 0.437455 (at node 13)
Accepted flit rate average= 0.432118
minimum = 0.423995 (at node 0)
maximum = 0.435935 (at node 5)
Injected packet length average = 1.79914
Accepted packet length average = 1.79915
Total in-flight flits = 60 (60 measured)
latency change = 0.00229864
throughput change = 0.00187377
Class 0:
Packet latency average = 7.43886
minimum = 1
maximum = 84
Network latency average = 5.70049
minimum = 1
maximum = 46
Slowest packet = 1151754
Flit latency average = 4.91757
minimum = 1
maximum = 46
Slowest flit = 4104614
Fragmentation average = 0
minimum = 0
maximum = 0
Injected packet rate average = 0.24003
minimum = 0.238893 (at node 6)
maximum = 0.242187 (at node 8)
Accepted packet rate average = 0.240031
minimum = 0.23827 (at node 14)
maximum = 0.241723 (at node 5)
Injected flit rate average = 0.43155
minimum = 0.427747 (at node 4)
maximum = 0.436627 (at node 8)
Accepted flit rate average= 0.431552
minimum = 0.427083 (at node 14)
maximum = 0.43452 (at node 2)
Injected packet length average = 1.7979
Accepted packet length average = 1.79791
Total in-flight flits = 46 (46 measured)
latency change = 0.00504286
throughput change = 0.00131043
Draining all recorded packets ...
Draining remaining packets ...
Time taken is 600044 cycles
====== Overall Traffic Statistics ======
====== Traffic class 0 ======
Packet latency average = 7.43885 (1 samples)
minimum = 1 (1 samples)
maximum = 84 (1 samples)
Network latency average = 5.7005 (1 samples)
minimum = 1 (1 samples)
maximum = 46 (1 samples)
Flit latency average = 4.91755 (1 samples)
minimum = 1 (1 samples)
maximum = 46 (1 samples)
Fragmentation average = 0 (1 samples)
minimum = 0 (1 samples)
maximum = 0 (1 samples)
Injected packet rate average = 0.24003 (1 samples)
minimum = 0.238893 (1 samples)
maximum = 0.242187 (1 samples)
Accepted packet rate average = 0.240031 (1 samples)
minimum = 0.23827 (1 samples)
maximum = 0.241723 (1 samples)
Injected flit rate average = 0.43155 (1 samples)
minimum = 0.427747 (1 samples)
maximum = 0.436627 (1 samples)
Accepted flit rate average = 0.431552 (1 samples)
minimum = 0.427083 (1 samples)
maximum = 0.43452 (1 samples)
Injected packet size average = 1.7979 (1 samples)
Accepted packet size average = 1.79791 (1 samples)
Hops average = 5.24839 (1 samples)
Total run time 10.81